## Slide 1
Ham Radio Report
Brad Denham – KF6PSL
Wednesday, June 14, 2023
Installation of
Yaesu FTM-400XDR 2M/440 Mobile Radio into 2006 Mazdaspeed 6

## Slide 2: Equipment Overview:
2006 Mazdaspeed 6 Sedan:
  Walmart “Everstart Platinum” Battery (new)
    AGM | Group 35 | 650 CCA
    Made by Johnson Controls
  110 Amp Alternator
  Stock Battery Cables / Wiring
  Yaesu Power Cable Hook-up
2019 Yaesu FTM-400XDR:
  2M/440 Dual Band Transceiver
  Yaesu “System Fusion”
    Analog FM
    C4FM Digital
  BIG Beautiful Display w/ Remote Mount
    Scope Screen
    Altitude Screen
    APRS® Screen
    Smart Navigation Screen
    Frequency Direct Input Screen
    Clock / Timer Screen
  50 W / 20 W / 5 W
  APRS & Cross-Band Capable
  Factory Installed GPS w/ Smart Navigation
Antennas:
  Comet #CA-2X4SR 2M/440 Mobile Antenna, PL-259, 40” (“Daily Driver”)
  MFJ #1432 2M/440 Mobile Antenna, PL-259, 62.5” (Event Support)
  Diamond #AZ507RSP Mobile Antenna, PL-259, Spring Base, 27.5" (Back-up)
  Diamond #K600S HD Trunk Lip Mount
Radio/Mic Mount:
  Lido Radio Products #LM-500-DB-AMPS Heavy Duty Ram 1" Ball Style Mount
  Lido Radio Products #LM-EXT-01 Extension Bracket
  Lido Radio Products #LM-1203 Mic Hanger
Remote Speaker:
  RoadPro #RP-160 6 watt 3½”x 5”
  B-pillar mounted (for now) at my left shoulder
  Cable is too short…will be relocated to the visor when I get a 3.5mm mono extension cable

## Slide 3: FTM-400XDR Radio Mounting:
The main FTM-400XDR radio body is located under the driver’s seat…
…mounted to a heavy plywood base proving air flow under and over the radio with the exposed cooling fan getting access to the coolest air
Power cables
Remote speaker cable

## Slide 4: Remote Head Mount:
The old LIDO Mount…
The NEW LIDO Mount…
Snapped!

## Slide 5: Remote Head Mount:
The NEW LIDO Mount…
https://www.lidoradio.com/
Mounted directly to lid of the center console storage tray

## Slide 6: Battery / Wiring:
Direct-to-battery power connections!
Dual inline fuses

## Slide 7: Remote Speaker Mount:
Kenwood #SP-50B Mobile Speaker mount (under-seat location)
  RoadPro #RP-160 6-watt 3½”x 5” “CB Radio” Speaker…
B-pillar mount (for now)

## Slide 8: Antennas & Mount:
Comet #CA-2X4SR
40”
Fold-over
MFJ #1432
62.5”
#K600S
Heavy Duty
Trunk Lip
SO-239
#AZ507RSP
27.5”
Spring base

## Slide 9: Antennas & Mount:
I tighten the four mounting set screws twice a year; no issues with the SO-239 mount with the long MFJ antenna @ highway speeds

## Slide 10: Future Plans/Upgrades:
Big Three Upgrade (supplemental 6AWG +/- electrical cables):
  Battery negative (-) to chassis
  Battery positive (+) to alternator output stud
  Alternator case to battery negative (-)
Supplemental 5-wire grounding kit: chassis to the engine block, trunk lid to body, negative (-) battery terminal to various locations, etc.) by Flex-Innovations: https://www.flex-innovations.com/new_page_2.htm
Dedicated 140 Ah Ham Radio Battery in Trunk (similar to the dedicated radio battery set-up that was in my ‘96 Bronco)
Powerwerx / West Mountain Radio DC Power products for battery power cables, battery charging & isolation, battery mount, etc.
Additional Lido mounts for Uniden BCD463HP and SC150B hand-held scanners

## Slide 11
2022 Huntsman SportsFest
2023 SLC Marathon
Thanks!
Brad Denham
KF6PSL
801-502-5094
kf6psl@gmail.com